## Slide 1
Design and implementation of an eBPF-based runtime security monitoring Tool
End-to-End Pipeline and Hook Implementation
Simone Romano

## Slide 2
Project Reference and Architectural Constraints
Not a Tracee replica, but a more focused and controllable runtime.
General-purpose, multi-kernel runtime security.
Ring buffer as the primary transport channel.
Reference for the probe registry, pipeline, and event model.
Targeted at Rocky Linux 8, kernel 4.18.
Adapted to verifier constraints and provable memory offsets.
Perf buffer as the main operational transport.
Lightweight policy layer.
Tracee - Reference
Our Approach

## Slide 3
End-to-End Architecture and Pipeline
Cobra CLI / YAML
Probe Registry / libbpfgo
eBPF Hook
Perf Buffer
Go Decoder
Normalized Event
Event Output
Policy & Detector
Alert Output
Runtime Diagnostics (Zap)
eBPF Kernel Space
Go Userspace
Cobra CLI: Parses configuration and initializes the runtime.
Collection and transport: eBPF hooks submit events through the perf buffer.
Routing: Normalized events are sent to raw output and the detection engine.

## Slide 4
Binary Contract and Event Normalization
Kernel
[ event_context_t + argnum + args buffer ]
Shared C/Go Registry
Userspace
Event: security_file_open
Path: /etc/shadow
Flag: O_RDONLY
From binary records
to typed, indexed arguments
Binary contract: Shared context, indexed arguments, and synchronized C/Go registries.
Unique mapping: eBPF event ID, event name, and decoding schema.
Enrichment: Userspace normalization of capabilities, flags, bitmasks, and errno values.

## Slide 5
Detector YAML Evaluates Threat Conditions
Policy and Detection Layer (YAML)
Policy YAML Selects What to Observe
Alert Output
Detection Result
Normalized Event
Selected Events
security_task_fix_setuid
(new_euid=0)
sched_process_exec
(uid=0)
Alert: Privilege Escalation
[MITRE: TA0004]
[Within t seconds]

## Slide 6
Kernel Hook Implementation Strategy
Semantic hooks: Primarily based on kprobes and security hooks exposing resolved kernel objects.
Enter/exit model: Entry stores arguments; exit adds the final return value.
Kernel adaptation: Designed around Rocky Linux 4.18 verifier constraints.
Required Information
Is the Return Value Required?
Normalized Event in Go Userspace
Enter/Exit Model
Semantic Hook
Yes
No

## Slide 7
Common eBPF Implementation Pattern
program_data_t
Per-hook working state
event_data_t
Event under construction
event_context_t
timestamp
event ID
task_context_t
args_buffer_t
Indexed and serialized arguments.
When the return value is required, entry stores the arguments and exit completes the event with the syscall outcome.
init_program_data()
save_to_submit_buf() /
save_str_to_buf() /
save_str_arr_to_buf()
events_perf_submit()
Context Initialization
Typed Serialization
Perf-Buffer Submission

## Slide 8
Process Lifecycle
fork / vfork / clone
Syscall Request:
Capture the initial process-creation request.
sched_process_fork
Parent-child relationship:
Observe the task relationship established by the kernel.
task_rename
Task transition:
Track changes to the process comm.
sched_process_exec
Executable image:
Confirm successful image replacement.
sched_process_exit
Termination:
Record process exit and exit code.

## Slide 9
Initial request
Execution Monitoring: Attempts and Outcomes
execve
execveat
security_bprm_check
Security Validation:
Observes executable-image security checks.
security_bprm_creds_for_exec
Credential preparation:
Observes credentials prepared for the new image.
sched_process_exec
Successful outcome: Confirms executable-image replacement.
process_execute_failed
Failed outcome: Reports isolated failures with a normalized errno.

## Slide 10
Identity, Credentials, and Capabilities
Previous Credentials
setuid / setgid Families
security_task_fix_setuid
commit_creds
Userspace Request
Security-Path Validation
Final Credential Commit
Capability and process control
cap_capable: Observes checks for specific capabilities.
ptrace and security_task_prctl: Observe direct process interaction and state manipulation.

## Slide 11
File, Permission, and Filesystem Security
File Access
open: reports the syscall outcome.
security_file_open / security_file_permission: expose stable metadata (path, inode, device, and ctime)
Mounting
security_sb_mount / security_sb_unumount: observe mount points and associated flags.
Inode
unlink, rename, symlink and mknod: track structural filesystem changes.
Permissions
The chmod and chown families monitor permission and ownership changes, including return values.

## Slide 12
Memory and Namespaces
Namespace Transitions
Memory Management
mmap
mprotect
pkey_mprotect
memfd_create
process_vm_readv / process_vm_writev
Visibility into executable-memory transitions, fileless execution, unusual mappings, and cross-process memory access.
setns
unshare
switch_task_ns
Observes isolation requests and verifies the namespace changes effectively applied by the kernel.

## Slide 13
Kernel Hardening and Modules
Example of a scenario observable through distinct events
module load
register_kprobe
procfs Entry
Module lifecycle:
module_load,
module_free,
do_init_module.
eBPF surface:
security_bpf,
security_bpf_map,
security_bpf_prog.
Dynamic instrumentation:
register_kprobe,
kallsyms_lookup_name.
Kernel interfaces:
proc_create,
call_usermodehelper,
security_kernel_read_file.

## Slide 14
Experimental Validation Setup
Monitor Pod
eBPF Agent
Filtering on UID 10001
Trigger Pod
Exploit Client
(Attacker)
Shared Linux Kernel (Rocky Linux 8.10)
Target Pod
Vulnerable CTF Service (UID 10001)
Contains Flag Secret
Attack sequence:
Exploit -> ROP chain
-> /bin/sh -> /bin/cat ->
File Exfiltration

## Slide 15
Evaluation Results: CPU Consumption
The prototype reduced mean CPU by about 92% through filtering before transport.
All retained runs recovered the flags and produced the required evidence.
Falco, Tetragon, and the prototype apply UID selection at different stages

## Slide 16
Conclusions
Key Findings
Kernel observations can be transformed into consistent security evidence.
Configurable monitoring supports different investigation task, useful for the security analyst.
Early filtering can reduce performance cost
Broader coverage and higher event rates remain future work.
Any question?